Section Cover Page

Section 02 91 19 Removal and Disposal of 2018-01-22 Ozone Depleting Substances (ODS)

Use this section to specify the removal and disposal of ODS-containing refrigerants.

This Technical Specification Section contains:

.1	This Cover Sheet

.2	Specification Text

### 1.	General

1.1	Section Includes

1.2	Disposal Contractor Qualifications

1.3	Regulatory Requirements

1.4	Worker Protection for ODS

### 2.	Products

Not Used

3.	Execution

3.1	ODS-Containing Refrigerant

1.	General

1.1	SECTION INCLUDES

.1	This Section includes requirements for identification, removal, preparation for disposal, transportation, and permanent disposal of refrigerants containing Ozone-Depleting Substances (ODS).

1.2	REMOVAL CONTRACTOR QUALIFICATIONS

.1	Use qualified refrigeration specialist for removal and disposal of ODS-containing refrigerant.

.2	The Refrigerant Management Canada (RMC) program shall be followed for disposal of ODS. For more information: http://www.refrigerantmanagement.ca/index.php

1.3	DISPOSAL CONTRACTOR QUALIFICATIONS

.1	ODS-containing refrigerant shall be disposed of by the refrigeration specialist.

1.4	REGULATORY REQUIREMENTS

.1	Comply with the following:

.1	Environmental Contaminants Act (Canada)

.2	Environmental Protection and Enhancement Act (Alberta)

.3	Transportation of Dangerous Goods Act, 1992 (Canada)

.4	Dangerous Goods Transportation and Handling Act (Alberta) and regulations

.5	Other legislation and regulations which apply to the performance of the work of this section.

1.5	WORKER PROTECTION FOR ODS

.1	Require workers to wear chemical resistant gloves when removing ODS where exposure risk is low.

.2	Provide workers with additional protective clothing and respiratory equipment where contact with ODS may occur.  Provide clothing and equipment appropriate for the potential level of exposure. Equipment may include chemical resistant gloves, coveralls, safety glasses with side shields, and respirator approved by the National Institute for Occupational Safety and Health (NIOSH) for ODS filtration.

2.	Products (Not Used)

3.	Execution

3.1	ODS-CONTAINING REFRIGERANT

.1	Locate all ODS-containing units.

.2	Refrigerant specialist shall remove all ODS including R-11, R-12 and R-22 refrigerant from the system it is used in, and re-cycle or dispose of properly.

.3	Absorb any spill with absorptive material and immediately ventilate area.

.4	Handle, store, transport and recycle ODS-containing refrigerants in accordance with Alberta and Federal legislation and regulations.

END OF SECTION