Section Cover Page

Section 07 21 23 2011-08-15 Granular Insulation

This Master Specification Section contains:

.1	This Cover Sheet

.2	Specification Section Text:

1.	General

1.1	Related Work Specified in Other Sections

1.2	Submittals

1.3	Delivery, Storage, and Handling

2.	Products

2.1	Materials

3.	Execution

3.1	Workmanship

3.2	Installation

1.	General

1.1	RELATED WORK SPECIFIED IN OTHER SECTIONS

.1	Waste Management and Disposal	Section 01 74 19.

.2	Masonry work to receive insulation:	Section 04 20 00.

.3	[                              ] insulation:	Section [            ].

.4	[                              ] insulation:	Section [            ].

1.2	submittals

.1	Comply with requirements of Division 01.

.2	Product Data:

.1	Submit manufacturer's printed product literature, specifications and data sheet in accordance with Section 01 33 00 - Submittal Procedures.

.2	Provide [two] [         ] copies of most recent data sheets describing materials' physical properties and include product characteristics, performance criteria, physical size, finish and limitations.

.3	Provide [two] [        ] copies of MSDS.

1.3	delivery, STORAGE, and handling

.1	Delivery and Acceptance Requirements:

.1	Deliver insulation and accessories in original unopened packaging or cartons bearing manufacturer's seals and labels.

.2	Pile bagged insulation neatly on raised platforms and protect with waterproof covers.

.2	Waste Management and Disposal:

.1	Separate waste materials for [reuse] [and] [recycling] in accordance with Section 01 74 19 - Management and Disposal.

2.	Products

2.1	MATERIALS

.1	Granular Insulation:  vermiculite or perlite granular fill, water repellent, rot and vermin proof, fire resistant flame/fuel/smoke rating of 0/0/0.

3.	Execution

3.1	WORKMANSHIP

.1	Install insulation after masonry materials are dry.

.2	Install insulation to maintain continuity of thermal protection to building elements and spaces.

.3	Install materials in accordance with manufacturer's instructions.

3.2	INSTALLATION

.1	Fill completely with insulation, the [cavity space between masonry wythes] [concrete block cores.]

.2	Plug all holes in wall through which insulation may escape, using glass fibre mesh.

.3	Caulk and seal around all door or window openings, electric outlets, pipes and all other openings.

.4	Pour directly into the wall from the bag or from a hopper placed on top of the wall.

.5	The height of pour shall not exceed 6 m or one storey height, whichever is less.

.6	Place temporary signs in all rooms on face of insulated wall warning all trades to use caution to prevent loss of insulation if cutting into the wall.

END OF SECTION