Section Cover Page

Section 26 01 90 Electrical Spare Parts 2018-06-12 and Maintenance Materials

Use this Section to specify all electrical spare parts and maintenance materials for Division 26, 27 & 28 (electrical equipment and systems).  Do not specify these requirements in individual technical sections; include cross-references to this Section 26 01 90 only.

In defining the items and quantities of electrical spare parts and maintenance to be provided under the contract, consider the following criteria:

.1	Project size and complexity.

.2	Project location.

.3	Class of building.

.4	Availability of items.

.5	Manufacturer's recommendations.

This Master Specification Section contains:

.1	This Cover Sheet

.2	Specification Section Text:

1.	General

1.1	Related Sections

1.2	Inventory List

2.	Products

2.1	Spare Parts and Maintenance Materials Schedule

2.2	Tools and Cabinets

3.	Execution

3.1	Delivery

1.	General

1.1	RELATED SECTIONS

.1	Spare Parts and Maintenance Materials:	Division 01.

1.2	INVENTORY LIST

.1	Submit a complete inventory list of electrical spare parts and maintenance materials delivered to the Minister.

2.	Products

2.1	SPARE PARTS AND MAINTENANCE MATERIALS SCHEDULE

| Item |  | Quantity |
| --- | --- | --- |
| SPEC NOTE: List in schedule form, all electrical spare parts and maintenance materials deemed necessary for the project and to be provided under the contract. Items and quantities listed below are intended as a general guide only. Modify items and quantities to suit project requirements. |
| .1 | Medium Voltage Switchgear: |  |
|  | .1 Drawout power circuit breaker complete with all accessories, frame size, [ ]: | One |
|  | .2 Fuses: | Three of each size and type |
|  | .3 [ ]: | [ ] |
|  | .4 [ ]: | [ ] |
| .2 | IACB Main Distribution Centre: |  |
|  | .1 Drawout industrial air circuit breaker complete with all accessories, frame size, [1600 A] [ A]: | One |
|  | .2 Fuses: | Three of each size and type |
| .3 | Emergency Generator: |  |
|  | .1 Oil filters: | Six |
|  | .2 Air filters: | Six |
|  | .3 Drive belts: | One set |
|  | .4 [ ]: | [ ] |

Continued next page

2.1	SPARE PARTS AND MAINTENANCE MATERIALS SCHEDULE (Cont’d)

| Item |  | Quantity |
| --- | --- | --- |
| .4 | Transfer Switch: |  |
|  | .1 Voltage sensing relays: | Two |
|  | .2 [ ]: | [ ] |
| .5 | Luminaires: |  |
|  | .1 Fluorescent ballasts: | One of each type |
|  | .2 LED drivers: | Two of each type |
|  | .3 [ ]: | [ ] |
| .6 | Lamps: |  |
|  | .1 Fluorescent lamps: | 12 of each size and type |
|  | .2 LED arrays/lamps: | 4 of each size and type |
|  | .3 [ ]: | [ ] |
| .7 | Lighting Control System: |  |
|  | .1 Low voltage relays: | Six |
|  | .2 Low voltage switches: | Six |
|  | .3 [ ]: | [ ] |
| .8 | Fire Alarm System: |  |
|  | .1 Products of combustion detectors: | [6] |
|  | .2 Thermal detectors: | Two of each type |
|  | .3 [ ]: | [ ] |
| .9 | Communications Systems: |  |
|  | .1 Intercom station: | One |
|  | .2 [ ]: | [ ] |

Continued next page

2.1	SPARE PARTS AND MAINTENANCE MATERIALS SCHEDULE (Cont’d)

| Item |  | Quantity |
| --- | --- | --- |
| .10 | Motor Control Centres: |  |
|  | .1 HOA selector switch: | Two |
|  | .2 Pilot lights: | 12 |
|  | .3 Operating coil for each size starter: | Two |
|  | .4 Control fuses: | Six of each size |
|  | .5 [ ]: | [ ] |
| .11 | [ ]: |  |
|  | .1 [ ]: | [ ] |
|  | .2 [ ]: | [ ] |
|  | .3 [ ]: | [ ] |
| SPEC NOTE: Add additional requirements to schedule as necessary to provide a comprehensive list of all electrical spare parts and maintenance materials required for project. |

2.2	TOOLS AND CABINETS

.1	Provide all special tools required for normal maintenance in a heavy gauge, corrosion resistant metal box complete with lock and keys.

.2	Provide wall mounted metal cabinet with adjustable shelving and hinged locking door to house all spare parts associated with power system.

3.	Execution

3.1	DELIVERY

.1	Deliver spare parts and maintenance materials to project site or other location designated by Minister and obtain receipt for materials delivered.

END OF SECTION