Section Cover Page

Section 27 10 20 2008-05-01 Telephone

Most lodges have a telephone service to each suite.  The incoming service is usually adequate.

Current standards require a "home-run" from each suite to the telephone board.  If the existing system is not of the "home-run" type, use this Section to specify one; use it also to specify any new outlets that may be required.

This Master Specification Section contains:

.1	This Cover Page

.2	Specification Section Text:

1.	General

1.1	Related Requirements

1.2	System

2.	Products

2.1	Components

3.	Execution

3.1	Installation

1.	General

1.1	RELATED REQUIREMENTS

.1	Electrical General Requirements:	Section 26 00 05.

1.2	SYSTEM

.1	Telephone cable run from each outlet noted, to the telephone board.

2.	Products

2.1	COMPONENTS

.1	Cable:  4-conductor, 24 AWG, FT4 telephone cable.

.2	Outlet:  RJ-11 female screw terminal type jack installed in a wall box c/w telephone coverplate.

.3	Boxes and fittings:  refer to Section 26 00 05.

3.	Execution

3.1	INSTALLATION

.1	Harness telephone cables together and run parallel and at right angles to building lines.

.2	Run feeds to satellite panels in conduit.

.3	Telephone cables may be run open but concealed in ceiling spaces and crawl spaces.

.4	Terminate telephone cable only at outlet in resident rooms.   Leave 4 m of slack cable at telephone terminal board.

SPEC NOTE:  Specify the following when new outlets are required.

.5	[Remove all existing wiring and outlets to telephones in resident rooms and replace with components specified.]

.6	Terminate and provide jacks for a complete system.

.7	Maintain service to each resident's room for the duration of the project.

END OF SECTION