Section Cover Page

Section 31 10 00 2018-08-15 Site Clearing

Refer to “LEED Notes and Credits” page for additional guidance for LEED projects. Delete LEED items if project: .1 is excluded by the Department’s policy on LEED, or .2 the Department has determined that the work of this Contract is not to attain a LEED rating.

Use this Section to specify requirements for general site clearing operations, including tree and vegetation removal, protection of existing trees that are to remain, removal of existing site improvements such as fencing that interfere with new construction or are otherwise required to be removed, and for timber salvaging.  This Section does not include for removal of topsoil or other excavation requirements.

Do not include this Section on all projects; include only on projects where site clearing is required, normally as a separate operation prior to excavation work.

This Master Specification Section contains:

.1	This Cover Sheet

.2	Specification Section Text:

1.	General

1.1	Related Requirements

1.2	Reference Documents

1.3	Protection

1.4	Delivery, Storage and Handling

1.5	LEED Requirements

2.	Products

Not Used

3.	Execution

3.1	Timber Salvaging

3.2	Clearing

3.3	Disposal

LEED Notes:

Refer to Section 01 35 18 – LEED Requirements for:

.1	Requirements necessary for this project to obtain points required for certification.

.2	Confirmation of LEED prerequisites and credits affecting this Section; not all are mandatory for certification

Maintain built-in sustainability regardless of LEED requirements for:

.1	Recycling, reuse of materials, components and assemblies.

.2	Diversion of construction waste from landfills.

.3	Use of recycled materials, local materials, rapidly renewable and durable materials.

.4	Maintain healthy indoor environment during constructing.

.5	Provide for thermal comfort, access to views and daylight for indoor spaces.

.6	Foster innovation into facility design and planning.

LEED Credits:

SPEC NOTE:  Though prerequisites do not contribute to a project point score, they are mandatory and MUST be met for a project to receive LEED certification.

Potential LEED credits available through this section:

Sustainable Sites

.1	SS Preresquisite – Construction Activity Pollution Prevention

Materials and Resources

.1	MR Prerequisite – Construction and Demolision Waste Management Planning

.2	MR Credit  – Construction Waste Management

END OF DATA SHEETS

1.	General

1.1	RELATED Requirements

.1	Building Demolition:	Section 02 41 16.

1.2	Reference documents

SPEC NOTE:  Delete LEED standards for projects not pursuing LEED certification.

.1	[Canada Green Building Council (CaGBC)

.1	LEED V4 Rating System, for Building Design and Construction. Website: www.cagbc.org]

1.3	PROTECTION

.1	Protect trees, shrubs and other vegetation indicated to remain in place, against unnecessary cutting, breaking and any other damage.

.2	Protect root systems exposed during clearing operations from damage.

.3	Protect fences, sidewalks, roadways and other existing site improvements that are to remain, from damage.

.4	Protect bench marks and reference lines from damage.

1.4	Delivery, Storage and Handling

.1	Separate waste materials for [reuse] [and] [recycling] in accordance with Section 01 74 19 – Waste Management and Disposal.

SPEC NOTE: Delete LEED submittal item if project is not to attain LEED certification or if the following credits are not being sought.

1.5	Leed requirements

.1	SS Prerequisite – Construction Activity Pollution Prevention:

.1	Objectives: reduce pollution from construction activities by controlling soil erosion, waterway sedimentation and airborne dust generation.

.2	Requirements: create and implement an erosion and sedimentation control plan for the Project as outlined in the LEED Rating System.

.2	MR Credit – Construction Waste Management:

.1	Objectives: divert land clearing debris and vegetation associated with site demolition from landfills.  Redirect demolished materials to an appropriate recycling facility.

.2	Requirements: track and record the amount of construction waste that is landfilled and the amount of construction waste that is recycled.  Submit calculations indicating that [50] [75][    ]% of construction waste was diverted from landfills.

2.	Products

.1	Not used.

3.	Execution

3.1	TIMBER SALVAGING

SPEC NOTE:  Include this article only when site contains salvageable timber, e.g. for projects located within provincial parks.

.1	Fell trees indicated to be removed, and which are 150 mm caliper size and larger, measured one metre above grade.  Leave not more than 400 mm high stump.

.2	Remove branches, and portion of trunk less than 100 mm diameter.

.3	Transport limbed logs to [location designated on drawings.] [following location:]

.1	[              ]

.4	Pile logs side by side to a height not exceeding 2.4 m.

.5	Space log piles as directed by the Province.

3.2	CLEARING

.1	Remove trees, stumps, shrubs, vegetation, loose surface rock, site improvements and other obstructions interfering with the Work or required to be removed.

.2	Dig out and remove trunks and root systems where no further excavation work is required.

.3	Carefully and cleanly cut roots and branches of trees indicated to remain, where such roots or branches interfere with new construction.  Treat freshly cut roots or branches with non-toxic horticulturally accepted emulsion.

3.3	DISPOSAL

.1	Debris to disposed of properly at an offsite facility.

END OF SECTION