Section Cover Page

Section 31 23 16 2018-08-15 Building and Structure Excavating

Use this Section to specify requirements which apply specifically to excavating for buildings and structures.  This Section excludes site excavating outside perimeter of building and structure excavations.

This Master Specification Section contains:

.1	This Cover Sheet

.2	Specifications Section Text:

1.	General

1.1	Related Requirements

1.2	Section Includes

2.	Products

3.	Execution

3.1	Excavation

1.	General

1.1	Related Requirements

.1	Read this Section in conjunction with:

.1	Earthwork General Requirements:	Section 31 20 10.

1.2	SECTION INCLUDES

.1	This Section includes requirements for excavating for buildings and structures inside perimeter of each building or structure, and within a nominal distance outside perimeter of each building or structure, as required for foundation and other substructure construction.

2.	Products

Not Used.

3.	Execution

3.1	EXCAVATION

.1	Excavate to elevations and dimensions indicated on Drawings within a tolerance of plus or minus [50] [    ] mm, and extending a sufficient distance from footings and foundation walls to permit placing and removal of concrete formwork, installation of services, other required construction, and for inspection.

.2	In excavating for footings and foundations, take care not to disturb bottom of excavation.  Excavate by hand to final grade just before concrete reinforcement is placed.

.3	Protect bottom of excavations and soil around and beneath footings from frost.

.4	Ensure that excavation meets the requirements set out in the Occupational Health and Safety Code, Part 32, Excavating and Tunnelling.

SPEC NOTE:  Expand requirements as appropriate for the project.

END OF SECTION