Section Cover Page

Section 31 23 35 Building and Structure 2018-08-15 Backfilling

Use this Section to specify requirements which apply specifically to backfilling and compaction of fill materials inside perimeter of or immediately adjacent to buildings and structures.  This Section excludes filling and grading outside perimeter of buildings or structures.

This Master Specification Section contains:

.1	This Cover Sheet

.2	Specification Section Text:

1.	General

1.1	Related Requirements

1.2	Section Includes

2.	Products

2.1	Materials

3.	Execution

3.1	Placement and Compaction of Fill Materials

3.2	Granular Base Construction Under Slabs

3.3	Backfilling and Filling Schedule

1.	General

1.1	Related Requirements

.1	Read this Section in conjunction with:

.1	[Earthwork Testing:	Section 31 00 10.]

.2	Fill Materials:	Section 31 05 13.

.3	Earthwork General Requirements:	Section 31 20 10.

1.2	SECTION INCLUDES

.1	This Section includes requirements for:

.1	Backfilling, filling, and compaction inside perimeter of each building or structure and outside perimeter of each building or structure, adjacent to foundations.

.2	Granular base construction, above subgrade, for floor slabs supported on grade, within perimeter of building or structure.

2.	Products

2.1	MATERIALS

.1	Refer to Section 31 05 13 for fill material product specifications.

3.	Execution

3.1	PLACEMENT AND COMPACTION OF FILL MATERIALS

.1	Backfill excavations and fill to required subgrade elevations using fill materials specified in Backfilling and Filling Schedule.

.2	Place fill materials in layers not exceeding loose thickness specified in Backfilling and Filling Schedule.

.3	Compact each layer of fill to the minimum percentages of Standard Proctor Density specified in Backfilling and Filling Schedule.

.4	Ensure that adequate permanent or temporary horizontal bracing [or diaphragm] is in place prior to backfilling against walls.

.5	When backfilling on either side of a wall member, keep the differential soil depth within [200] mm.

.6	Take care to prevent damage to or displacement of waterproofing, insulation, weeping tile installation, pipe, conduit and other work.

3.2	GRANULAR BASE CONSTRUCTION UNDER SLABS

.1	Directly under floor slabs supported on grade, provide a minimum [150] [        ] mm thick compacted layer of [25 mm crushed gravel] [                                          ].

.2	Where slab is to be directly underlain by a sheet moisture/vapour barrier, provide a uniform top dressing of coarse sand, applied and compacted to produce a smooth surface to receive sheet and slab.

3.3	BACKFILLING AND FILLING SCHEDULE

| Location | Fill Material | Max. Lift Thickness | Minimum Compaction |
| --- | --- | --- | --- |
| Under interior slabs-on-grade | [ ] | [ ] mm | [ ] % |
| Under exterior slabs-on-grade | [ ] | [ ] mm | [ ] % |
| Against exterior side of foundations and under paved areas | [ ] | [ ] mm | [ ] % |
| Against exterior side of foundations and under landscaped areas | [ ] | [ ] mm | [ ] % |
| SPEC NOTE: Modify above location descriptions or add additional location descriptions as required to clearly identify all locations where backfilling or filling is required. |
| [ ] | [ ] | [ ] mm | [ ] % |
| Other locations | [ ] | [ ] mm | [ ] % |

END OF SECTION