Section Cover Page

Section 32 99 06 2017-04-05 Modified Exterior Grounds Maintenance

This Master Specification Section contains:

.1	This Cover Page

.2	Specification Section Text:

1.	General

1.1	Scope of Work

1.2	Reference Standards

1.3	Hours of Work

1.4	Maintenance Log and Payments

1.5	Testing

1.6	Quality Assurance

1.7	Delivery, Storage and Handling

1.8	Examination of Site

1.9	Damage to Property

2.	Products

2.1	Fertilizer

2.2	Topsoil and Peatmoss

2.3	Plant Protection Materials

2.4	Pest Controls

2.5	Maintenance Schedule

2.6	Annual and Perennial Flowers

3.	Execution

3.1	General Workmanship

3.2	Spring Clean-Up and Preparation

3.3	Turf Maintenance

3.4	Tree and Shrub Maintenance

3.5	Annual Plant Bed Maintenance

3.6	Integrated Pest Management

3.7	Pests: Weed, Insect and Disease Control

3.8	Irrigation System

3.9	Autumn Preparation

3.10	Cleanliness of Grounds

.3	Data Sheet – Price Summary Schedules:

.1	Sample “A” – Grounds Maintenance Cost Summary

.2	Sample “B” – Grounds Maintenance Additional As-Required Work

Price Summary Schedule

Following are two sample schedules:

Sample “A” – Ground Maintenance Cost Summary

Sample “B” – Ground Maintenance Additional As-Required Work

These sample schedules or a derivative there of may be used to communicate to Infrastructure – Property Management the results of tendered and/or negotiated prices obtained for ground maintenance work that will be performed during the current ground maintenance season and costs for additional as-required work that may be requested to be performed during this maintenance season.

END OF DATA SHEET

| Grounds Maintenance Cost Summary |
| --- |
| Site Description: | Neil Crawford Provincial Centre |
| Location | Edmonton, Alberta |
| TPM Contactor: | XYZ Realty Ltd. |
| The following Schedule is a summary of the costs obtained for grounds maintenance work at this site. |
| ITEM NO. | DESCRIPTION OF WORK | UNIT | ESTIMATED QUANTITY | UNIT PRICE | EXTENDED AMOUNT |
| 1. | Zone 1 Turf: mowing, trimming, edging, clean-up, pest & turf irrigation monitoring requirements, and other specified turf work. | per cut | ________ | $________ | $__________ |
| 2. | Zone 2 Turf: mowing, trimming, edging, clean-up, pest & turf irrigation monitoring requirements, and other specified turf work. | per cut | ________ | $________ | $__________ |
| 3. | Zone 3 Turf: mowing, trimming, edging, clean-up, pest monitoring requirements, and other specified turf work. | per cut | ________ | $________ | $__________ |
| 4 | Turf Fertilization: spring application for all zone 1 and 2 turf areas as specified. | Lump sum | Lump sum | Lump sum | $__________ |
| 5 | Turf Fertilization: summer application for all zone 1 turf areas as specified. (Service to be performed on request only). | Lump sum | Lump sum | Lump sum | $__________ |
| 6. | Turf Aeration: Zone 1 (on request only). | task | ________ | $________ | $__________ |
| 7. | Turf Dethatching: Zone 1 (on request only). | task | ________ | $________ | $__________ |
| 8. | Spring Clean-Up & Preparation: complete site clean-up and preparation services including mechanical power sweeping as specified. | Lump Sum | Lump Sum | Lump Sum | $__________ |
| 9. | Autumn Clean-Up & Preparation: complete site clean-up and preparation services as specified. | Lump Sum | Lump Sum | Lump Sum | $__________ |
| 10. | Tree & Shrub Maintenance: all required plant maintenance services, plant health and pest monitoring requirements, and other tasks and work as specified. | month | ________ | $________ | $__________ |
| 11. | Grounds clean-up requirements as specified. | month | ________ | $________ | $__________ |
| 12. | Cash Allowance (additional as-required work). | Lump Sum | Lump Sum | Lump Sum | $__________ |
| Total Amount of Bid $______________ |

| Grounds Maintenance Additional As-Required Work |
| --- |
| Site Description: | Neil Crawford Provincial Centre |
| Location | Edmonton, Alberta |
| TPM Contactor: | XYZ Realty Ltd. |
| The following is a summary of rates obtained for performance of additional as-required work for grounds maintenance at this site. |
| ITEM NO. | DESCRIPTION OF WORK | UNIT | ESTIMATED QUANTITY | UNIT PRICE |  |
| 1. | Plant Watering Services: supply of water, water truck (minimum 2000 gal.), labour, accessories and applying water during growing season for selected established plants, for newly installed plant material and for winter preparation. | per truck load | __________ | $_________ | $_________ |
| 2. | Grounds Clean-Up Services: additional or emergency grounds clean-up tasks when necessary. | per site visit | __________ | $_________ | $_________ |
| 3. | Pest Controls: supply and application of approved pesticides to eliminate and control weed growth on all turf and hard surfaces. | application | __________ | $_________ | $_________ |
| 4. | Plant Pest Controls: supply and application of approved pesticides to control pests on plant material. | hour | __________ | $_________ | $_________ |
| 5. | Annual Plants: supply, installation and maintenance of flowering plants. | lump sum | lump sum | lump sum | $_________ |
| Total Amount $ |

# 1.	General

# 1.1	SCOPE OF WORK

.1	Provide grounds maintenance services that result in aesthetically pleasing and desirable site appearances.  Grounds maintenance services include all tasks, equipment, labour, materials and incidentals necessary to satisfactorily complete specified grounds maintenance services.  Work shall be performed to best horticultural and site cleanliness practices and standards acceptable to Property Manager.

# 1.2	REFERENCE STANDARDS

.1	“Alberta Yards & Gardens, What to Grow” published by Alberta Agriculture and Rural Development, Agdex 200/32-1.

.2	“Backyard Pest Management” published by Alberta Agriculture and Rural Development, Agdex 605-2.

.3	“Pruning in Alberta” published by Alberta Agriculture and Rural Development, Agdex 270/24-1.

.4	“Manual for Maintenance of Grounds” published by Infrastructure.

# 1.3	HOURS OF WORK

.1	Perform maintenance work during regular working hours of 7:00 a.m. to 6:00 p.m., Monday to Friday except where directed otherwise by Property Manager.

.2	Obtain Property Manager’s approval to perform maintenance outside of regular working hours.

# 1.4	Maintenance log and payments

.1	Complete grounds maintenance log (Schedule ‘A’) for each day of maintenance activity.

.2	Maintenance log shall be kept at Property Manager’s site office unless directed otherwise.  Contractor’s site supervisor shall complete, sign and submit maintenance log at completion of work each day.

.3	Property Manager reserves the right to reduce monthly payments when:

.1	contractor submits false maintenance log data,

.2	unsatisfactory, inadequate or incomplete site maintenance services are provided,

.3	inadequate or improper materials are supplied and used on site,

.4	contractor fails to perform required maintenance services on schedule.

.4	Contractor’s Invoice:  obtain Property Manager’s approval for completed work before submitting invoice.  Payment of contractor’s invoice must be supported with verifiable maintenance log data and other required submittals as specified.

.5	Record and update all maintenance activities including date/time of activities, materials and quantity used on site, location where activities were carried out, number of employees and name of supervisor on site.

# 1.5	TESTING

Additional As-Required Work:  soil analysis tests using an accredited testing laboratory shall be considered as additional as-required work in contract when requested by Property Manager.  Contractor shall submit cost estimate for Property Manager’s review and approval that will be based on Property Manager’s soil testing needs.

# 1.6	quality assurance

.1	Regulatory Requirements:  perform work in accordance with all applicable laws, codes and regulations required by authorities having jurisdiction over such work.  Submit copies of all permits and licenses required by local authorities.

.2	Site Supervisor:  shall be competent, experienced and knowledgeable to direct and supervise all staff and maintenance work of contract.    Supervisor shall either possess a Landscape Journeyman Gardener certification or have other horticultural qualifications and grounds maintenance experience acceptable to Property Manager to work on contract.  Approved site supervisor shall be on site during work of contract.  Submit supervisor’s credentials for Property Manager’s approval prior to commencement or work.

.3	Weekly Site Visits:  provide adequate site visits each week with sufficient staff and equipment to ensure all required maintenance services and tasks are performed and completed on schedule.

.4	Staffing:  provide experienced, competent and trained grounds maintenance personnel to perform all tasks and services in a safe and professional manner.  Contractor shall not assign any worker that Property Manager deems incompetent, careless, insubordinate, or otherwise objectionable to work on site grounds.

.5	Vehicles/Equipment:  appropriate and well maintained equipment, tools and other accessories shall be supplied to efficiently and effectively complete all required maintenance services.  Equipment shall have proper safety devices maintained at all times while in use.  Contractor’s vehicles shall be identifiable with company name and contact number.

.6	Employee Attire/Safety Vests:  all workers shall be properly attired at all times.   Each employee working on site shall wear a reflective coloured safety vest for safety and visibility.

.7	Site Inspections:  Property Manager shall, at their discretion, conduct random site inspections to evaluate the quality and completion of work performed.  Deficient work shall be promptly corrected.  Each month, the Contractor and Property Manager shall meet to review Contractor’s workmanship and performance.

.8	Site Security:  Contractor’s personnel shall carry personal identification at all times while on site.  All employees must check in with Property Manager upon entering and leaving the premises where applicable.

.9	Safety Precautions:  Contractor shall ensure that all employees use appropriate personal protective equipment where there is a danger of injury and as required by Alberta’s Occupational Health and Safety Act, Regulations and Code.  Essential protective equipment must meet CSA approval.  Contractor shall instruct all employees in appropriate safety measures and shall not permit the use or placement of equipment and tools in such a manner as to create safety hazards.

# 1.7	DELIVERY, STORAGE AND HANDLING

.1	No equipment or materials shall be stored on site.  Contractor shall remove all equipment and material off site each day to Contractor’s own storage space.

.2	Leave tools, equipment and materials in a secure storage area when not in use during period of operation and at the completion of each scheduled task.

.3	Contractor shall be present to accept delivery of all equipment and/or material shipments. Property Manager will not knowingly accept, unload or store anything delivered to site for Contractor’s use.  Inadvertent acceptance of delivery by Property Manager shall not constitute acceptance or responsibility for any of the materials or equipment.

# 1.8	EXAMINATION OF SITE

.1	Within ten days of commencement of contract thoroughly inspect and examine existing landscape conditions on site.

.2	Prepare a list of all plants and turf areas that are dead, unhealthy or damaged.  List other landscape features such as irrigation sprinkler heads, hard surfaces, furnishings and other items of maintenance that are deficient or damaged and require correction.  Take and submit photos to support list of deficient items.

.3	Submit required list and review with Property Manager for approval.  Failure to submit and review required list of existing conditions with Property Manager may result in Contractor being responsible for correction.

# 1.9	DAMAGE TO PROPERTY

.1	Contractor shall be held directly responsible for all damages to the property, the personal property of all site employees, staff and visitors and the property of adjacent land owners resulting from the actions of the contractor, the contractor’s employees, subcontractors or representatives who provide service under this contract.

.2	Contractor shall immediately report all damages to Property Manager.

.3	Repair, replace or restore all damaged property to its original condition or better as directed by the Property Manager.  Damages shall be promptly corrected within seven (7) days, unless directed otherwise by Property Manager.  Contractor shall be responsible for all costs to correct damaged property.

.4	Scalping of turf, mechanical damage or injury to plants, improper plant pruning, and damages resulting from improper use of chemical pesticides and fertilizers will be considered damage.

# 2.	Products

# 2.1	FERTILIZER

.1	Synthetic Turf Fertilizer:  apply a complete premium grade fertilizer, granular in composition, with over 50% of total nitrogen derived from a slow or controlled release nitrogen source.  No other type of fertilizer will be accepted for use on site.  Fertilizer shall contain all essential macronutrients plus 1%-2% iron and other micronutrients to maintain turf in a healthy, vigorous and green condition.

.2	Do not use any "weed and feed" fertilizer.

.3	Liquid turf fertilizers require Property Manager’s approval before use.  Liquid fertilizers shall be in a slow or controlled release form and equivalent to specified synthetic fertilizer regarding nutrient content and application rate.  Submit manufacturer’s data sheet showing percentage of each essential nutrient and provide information regarding mixture formula, rate of application and method.  Submit sample of liquid fertilizer mixture at time of application as requested by Property Manager.

.4	Plant Fertilizer:  apply premium grade fertilizer for plants and annuals in accordance with soil analysis (if applicable) or as directed by Property Manager.  Use only slow or controlled released fertilizers.

# 2.2	TOPSOIL AND PEATMOSS

.1	Imported Topsoil:  supply natural, fertile, friable, shredded, screened agricultural soil that can support healthy and vigorous plant growth as necessary in performance of specified tasks.  Topsoil shall be free of perennial weeds and grass, all other foreign matter and toxic materials.  Soil shall have a texture designated as “loam topsoil”.

.2	Sphagnum Peatmoss:  supply air-dried horticultural peatmoss packed in standard bags in performance of specified tasks.

# 2.3	PLANT PROTECTION MATERIALS

.1	Rodent, Animal and Sun Protection:  supply the following or similar as necessary;

.1	Woven wire mesh:  galvanized woven wire strands, 1.2 mm wire diameter or suitable alternative with an opening of 12.5 x 12.5 mm, c/w fasteners.

.2	Plastic:  perforated white spiraled strip.

# 2.4	PEST CONTROLs

Contractor Responsibilities In Contract: - Contractor shall monitor plant health in performance of maintenance services and advise the Property Manager on any potential pest problems.

Additional As-Required Work: - supply and application of chemical pesticides to control pests shall be considered as additional as-required work in contract.  Contractor shall submit cost estimate based on either an hourly rate or a lump sum rate as directed by Property Manager.  Service shall only proceed if approved by Property Manager.  Property Manager reserves the right to obtain competitive quotes from other contractor’s that specialize in pest control services.

.1	Chemical Pest Control:  supply and apply required chemical pesticides including herbicides, insecticides and fungicides, when necessary, to control or suppress pest populations on site.  Submit the following information for review and approval before applying any pesticide:

.1	Identification of specific pest(s) on site that require control.

.2	Trade name of chemical pesticide and manufacture’s instructions for use.

.3	Manufacturer’s material safety data sheets for each chemical pesticide.

.4	Name and credentials of licensed pesticide applicator.

.2	Pesticide Application Records:  pesticide application records shall be kept by certified applicator in accordance with Alberta Environment Protection and Enhancement Act.  Submit record books at completion of each pesticide application.  Provide information regarding target weed, insect or other pest, mode, type, and rates of application and results.  Include date, time, weather conditions and name of applicator.

# 2.5	MAINTENANCE SCHEDULE

.1	Schedule:  submit a neat, legible and detailed maintenance schedule at commencement of maintenance each spring.  List all weekly and monthly maintenance services and tasks specified in contract documents with approximate dates for completion.  Review schedule with Property Manager for approval.

2.6	ANNUAL AND PERENNIAL FLOWERS

Additional As-Required Work: - the supply, installation, and maintenance of annual flowering plants shall be considered as additional as-required work in contract when requested by Property Manager.  Contractor shall submit a lump sum cost estimate covering all required work for Property Manager’s review and approval.  Work shall only proceed if approved by Property Manager.  Property Manager reserves the right to obtain competitive quotes from others if necessary.

.1	Annual Plants:  supply and install all flowering, ornamental grass and other annual plants for each designated annual plant bed and container.  Provide a legible plan(s) showing proposed planting layout complete with plant variety, quantity and container size for each planting location for Property Manager’s review and approval minimum one month prior to installation.  Plan shall be prepared by an experienced landscape gardener who specializes in annual planting arrangements.  Property Manager reserves the right to determine what annual plant species, varieties or cultivars are to be supplied and planted on site.  All annual plants and plantings to meet the following requirements:

.1	Flowering plants shall be of superior quality, healthy and dense in appearance, and free of any disease and pests.

.2	Plants with elongated stems, widely spaced leaves, soft or discoloured spots, root bound containers, pest and wilting damage are not acceptable.

.3	Layout and installation of annual plants shall ensure that plants are spaced about 150 mm on centre to achieve a full, complete and appealing appearance.  Selected individual and larger growing plant species shall be spaced accordingly.

.4	Substitutions are unacceptable without prior approval of Property Manager.  Provide Property Manager with list of alternative plants only if specified flowering plants are unavailable or of unacceptable quality.  Provide list of growers contacted regarding availability.

.5	Provide annual plants in bud stage, just prior to first bloom, hardened off and ready for planting.

.6	Nursery Container Size For Annual Plants:  plants shall be grown and supplied in minimum P18 and larger sized nursery containers as appropriate for annual plant variety for acceptance.  Plants supplied in undersized or damaged containers are not acceptable.

.2	Annual Plant Inspection:  Contractor shall arrange for Property Manager’s inspection and approval of all flowering plants at local source of supply prior to purchase (if requested by Property Manager) and/or on site prior to installation.

.3	Property Manager reserves the right to reject any annual flowering plant found to be unhealthy or unappealing prior to or after installation.  Contractor shall immediately remove from site all plants deemed unacceptable by Property Manager and install new healthy flowering plants within three days at no additional cost.

# 3.	Execution

# 3.1	GENERAL WORKMANSHIP

.1	Property Manager will be the “Sole Judge” for assessing Contractor’s maintenance performance and workmanship.

.2	Schedule timing of operations based on plant growth, weather conditions and use of site.  Do each operation continuously and complete within reasonable time period.

.3	Do not perform work in any location or manner that may endanger the health and safety of the public.

.4	Collect and dispose of excess material and debris to approved municipal disposal site immediately following collection.

.5	Coordinate all maintenance practices with Property Manager.  Maintenance schedule shall be altered, when necessary, to accommodate site activities.

.6	Contact Property Manager when specified maintenance requirements cannot be met for any reason.

.7	Submit name and contact number of company representative for immediate or emergency service when necessary.

.8	Contractor’s principal owner and site supervisor must attend all site meetings held by Property Manager to review workmanship and performance.

.9	Contractor shall promptly correct all maintenance deficiencies noted by Property Manager during site meetings or following notification of site inspection results completed by Property Manager.  Deficient work or services shall be corrected by Contractor within two days of notification unless directed otherwise.

# 3.2	SPRING CLEAN-UP and preparation

.1	Complete spring clean-up by May 15th or as soon as working conditions are favourable.

.2	Thoroughly sweep, clean, collect and remove from site all sand, rock chips, salt and other debris accumulated during winter months from all maintained turf and hard surface areas.  Dispose of all collected material in approved municipal disposal site.

.3	Remove and store on site all stakes, sand/rock chip containers and other materials supplied by Property Manager.  Contractor supplied materials shall be removed off site.

.4	Collect and remove from site all dead vegetation, leaves, litter, and other debris from turf areas.  Rake clean dead patches of grass and fungal growth in lawn areas resulting from snow mold, where existing.

.5	Lightly roll turf areas where grass has lifted due to frost action (if applicable).

.6	Clean all plant/annual beds, tree wells, hedges, gravel/rock beds and other landscaped areas of all plant debris, weeds, leaves, litter, and other undesirable foreign matter and plant growth.  Reinstall loose plant bed edging materials as necessary.  Remove all collected debris and materials from site.

.7	Remove dead and unhealthy shrubs and other small plants including roots from site.  Fill plant pit with fertile topsoil.  Place topsoil to fill all low and uneven areas in plant beds.

.8	Loosen and lightly cultivate all non-mulched planting soil without disturbing roots of permanent plantings.  Edge all plant beds evenly to depth of 100 mm using a sharp spade to make an angled cut.  Remove resulting edging debris from site.

.9	Sweep and clean all hard surfaces including along all curbs and gutters.

.10	Mechanized Power Sweep:  power sweep all paved roadways, parking areas and other hard surfaces on site.  Coordinate task of power sweeping with Property Manager to minimize conflicts with facility and site users.  Perform work during non-regular working hours until complete. Provide mechanized power sweep services each spring and complete by May 15th.

# 3.3	TURF MAINTENANCE

.1	Turf Aeration:

Additional As-Required Work: - turf aeration shall only be performed when requested or deemed necessary by Property Manager.  Contractor shall submit a unit price bid in contract to perform turf aeration on selected turf locations.  Required services, however, shall only proceed upon Property Manager’s authorization.

Other additional turf areas in Zone 2 that may require aeration shall only proceed following approval of Contractor’s submitted bid price or cost estimate by Property Manager.

.1	Identify all sprinkler heads and other obstructions with flags before aerating.

.2	Turf Zone 1: aerate all turf areas in late September when directed by Property Manager.  Turf aeration shall generally be performed every two years with Property Manager’s authorization.  Ensure soil has adequate moisture before aerating.

.3	Turf Zone 2: aerate only turf areas containing compacted soil conditions such as pedestrian trails, vehicular traffic damages, parking islands, areas of site displays,  and other areas of compacted soil when directed by Property Manager.  Service shall generally be performed every two years if approved by Property Manager.   Ensure soil has adequate moisture before aerating.

.4	Use a vertical motion coring aerator with hollow tines that will penetrate the lawn, extract and deposit soil cores.  Aeration cores shall be minimum 50 mm depth and spaced no further than 90 mm apart.

.5	Aerate in minimum two different directions to obtain good coverage.  Remaining soil cores shall be left on turf areas during late fall.

.6	Contractor shall repeat turf aeration where coring depth or spacing are deficient or inadequate as directed by Property Manager.

.2	Dethatching:

Additional As-Required Work:  - turf dethatching shall only be performed when requested or deemed necessary by Property Manager.  Contractor shall submit a unit price bid in contract to perform turf dethatching on selected turf locations.  Required services, however, shall only proceed upon Property Manager’s authorization.

Other additional turf areas in Zone 2 that may require dethatching shall only proceed following approval of Contractor’s submitted bid price or cost estimate by Property Manager.

.1	Identify all obstructions in turf with flags before dethatching.

.2	Turf Zone 1: use adjustable power rake to dethatch all lawn areas during early spring.  Turf dethatching services shall generally be performed every two years if approved by Property Manager.  Remove all thatch and debris after turf areas are dethatched.

.3	Topdressing and Reseeding:

.1	Contractor shall topdress and reseed deficient and unhealthy turf areas that have been damaged by any means or cause resulting from Contractor’s workmanship unless directed by Property Manager to install new replacement sod.

.2	Mow deteriorated grass areas to height of 40 mm.  After mowing, rake thoroughly, removing loose and dead grass, stones and debris.

.3	Spread fertile topsoil to maximum thickness of 15 mm, filling in low areas and bare spots.  For severely damaged turf areas place sufficient topsoil and rake level with finish grade.

.4	Overseed turf areas with a quality seed mixture (approved by Property Manager) to match existing grass using a broadcast spreader.  Seed heavily at rate of minimum 4 kg/100 m2.  Rake seed into topsoil.  Roll lightly as necessary.  Apply appropriate fertilizer to all seed repairs.

.5	Apply water as necessary to seeded areas.  Maintain seed repairs as necessary to ensure healthy and vigorous growth.

.6	Additional As-Required Work: other deficient and unhealthy turf repairs that show root growth failure, deterioration, bare or thin spots shall only be repaired or restored upon Property Manager’s request.  Services shall only proceed following approval of Contractor’s cost estimate by Property Manager.  Property Manager reserves the right to obtain competitive quotes from other contractors to perform the work.

.4	Sod Replacement:

.1	Contractor shall replace and repair established turf areas that have been damaged by any means or cause resulting from Contractor’s workmanship.  Damages considered too small for sod replacement shall be repaired with topsoil and grass seed with Property Manager’s approval.

.2	Cut out and remove square or rectangular areas of dead, damaged and unhealthy turf using mechanical sod cutter and hand tools.

.3	Rake existing topsoil and apply appropriate fertilizer before installing new sod.  Spread adequate topsoil to fill uneven and low areas.

.4	Butt new sod tightly to adjacent existing sod.  Finish grade of new sod shall match adjacent undisturbed turf.  Place topsoil to fill open and exposed joints.

.5	Apply water at frequent intervals until new sod is well established.

.6	Additional As-Required Work: other deficient and unhealthy turf repairs that require new sod shall only be repaired or restored upon Property Manager’s request.  Services shall only proceed following approval of Contractor’s cost estimate by Property Manager.  Property Manager reserves the right to obtain competitive quotes from other contractors to perform the work.

.5	Fertilizing - Generally:

Additional As-Required Work: all applications of turf fertilizer must be approved by Property Manager.  Contractor shall submit a unit price bid in contract for each specified application of turf fertilizer.  Services, shall only proceed if authorized by Property Manager. However, the Property Manager reserves the right to obtain competitive quotes from other contractors that specialize in turf fertilization services.

.1	Apply fertilizer as specified.  Use mechanical equipment to spread fertilizer.  Check calibration of spreader to ensure specified application rate is used.

.2	Spread 50% of fertilizer in one direction, then 50% at right angles.

.3	Synthetic Fertilizer:  apply the following granular fertilizer unless directed otherwise by Property Manager.

.1	Spring Application:  all Zone 1 and 2 turf areas.  Apply 26-10-15 slow release granular fertilizer or similar at rate of 3.0 kg/100 m2 by May 25th.

.2	Summer Application:  all Zone 1 turf areas.  Apply 24-0-12 slow release granular fertilizer or similar at rate of 3.0 kg/100 m2 by July 15th.

.4	Water shall be applied immediately after fertilizing.  Use underground irrigation system (if applicable).  Preferably, the Contractor shall time fertilizer applications prior to a natural rainfall that will activate the fertilizer and produce the desired response.  Alternatively, the Contractor shall provide water, trucking and all other necessary equipment to apply adequate water in accordance with fertilizer manufacturer's recommendations at no additional cost to Property Manager.  Obtain moisture penetration of 50 mm minimum.

.5	Advise Property Manager prior to each application of turf fertilizer.  Contractor shall indicate total quantity (kilograms or other) of fertilizer applied on site in maintenance log after each application and submit other verifiable proof to support quantity of fertilizer applied on site upon completion of work.

.6	Inadequate, incomplete or improper applications of fertilizer will be considered unacceptable by Property Manager.  Applications of turf fertilizer shall not be approved by Property Manager until acceptable results are verifiable on site.

.6	Watering - Mowed Areas:

.1	Areas with underground irrigation systems:  operate systems as necessary and as directed by Property Manager.

.2	Areas with no underground irrigation systems:  supply labour, hoses, and sprinkler equipment to provide any required watering that can be performed using available building water source.

.3	Additional As-Required Work: when required and directed by Property Manager provide clean water, water truck, labour and accessories to provide turf watering services in areas with no source of available water or where directed by Property Manager.  Contractor shall submit cost estimate for Property Manager’s approval and authorization of service.

.4	Apply sufficient water, when required, to keep turf and underlying soil from drying out and to maintain healthy vigorous growing conditions.  Avoid shallow and frequent watering.  Apply water during early morning to achieve effective use of water.

.5	Watering of turf, using irrigation systems, shall be completed between 5:00 a.m. and 7:00 a.m., where applicable.  Provide 25 to 40 mm of water weekly including natural rainfall to wet upper 100 to 150 mm of soil.

.6	Adjust irrigation schedule due to natural precipitation.  During periods of drought stress, apply additional water to maintain healthy turf conditions.

.7	Mowing - Generally:

Note: - Contractor shall space turf cuttings at appropriate intervals from May to October to accommodate seasonal turf growth conditions and a reduced need to mow turf.  Property Manager, however, reserves the right to cancel any turf cutting that may be scheduled if deemed unnecessary or undesirable due to climatic conditions and turf health.  Property Manager, also, reserves the right to direct the Contractor’s scheduled turf cuttings and to adjust mowing heights when necessary.  Contractor shall only be paid for turf mowings and related work completed for each turf zone.

.1	Mowing Height:  turf zones shall be cut at required minimum heights that will vary during the season.  During periods of active growth turf shall be mowed at a lower mowing height.  Increase mowing heights during periods of slower growth.

.1	Turf Zone 1:  cut and maintain turf areas at 60 - 80 mm height during growing season.

.2	Turf Zone 2: cut and maintain turf areas at 80 - 100 mm height during growing season.

.3	Turf Zone 3: cut and maintain native turf areas at minimum 150 mm height.  Turf areas shall be mowed twice during the landscape season or as determined by Property Manager.  Mowing shall occur at appropriate intervals or when directed by Property Manager.

.2	Mowing of turf zones 1 and 2 shall be spaced on irregular and extended timeframes to accommodate the reduced quantity and need for turf mowing and maintenance.    Scheduled mowings shall vary during the landscape season from a more regular occurrence during active growing conditions to a ‘when required’ occurrence due to seasonal climatic conditions and inadequate turf growth.  Contractor shall never mow turf when insufficient growth has occurred or cut turf lower than specified height as the work will be considered unacceptable.  All mowings shall be scheduled in consultation with Property Manager.

.3	Mowing shall not be performed on wet turf.  Mower blades shall be kept sharp and properly adjusted to provide a cleanly cut grass blade.  Grass blade bruising, tearing and shredding is not acceptable.

.4	Remove all papers, rocks, animal waste, and other foreign material from turf areas before cutting grass.

.5	Remove grass clippings from site after each turf mowing.  However, short, fine and unnoticeable grass clippings may be left on lawns that are regularly mowed. In Zone 3 turf areas, remove accumulations of grass clippings deemed excessive by Property Manager.

.6	Mowing patterns or directions shall be rotated with each mowing where feasible to prevent rutting and minimize compaction.

.7	During each cutting operation, temporarily relocate movable site furnishings.  Replace to approximate original location after mowing lawn.

.8	Clean all sidewalks, stairs, roads, curbs, gutters, building walls and other hard surfaces of all grass clippings after each mowing using a vacuum or blower.  Remove clippings from site to maintain clean site appearances.

.9	Trimming:  trim grass areas as follows:

.1	trim grass along fences, walls, sign posts, structures, utility poles and other obstacles not accessible to mowers using a mechanical trimmer at height no lower than 70 mm.  Do not scalp turf or damage any plant material when using trimmers.  Remove resulting plant debris from site.

.2	use hand trimmers when necessary to trim grass adjacent to deciduous trees and other plants to prevent damage to tree trunks, plant stems and roots.  Avoid use of string line trimmers adjacent to plant materials.

.3	cut and hand trim grass around irrigation equipment, manholes, valves and other surface features in lawn areas using hand trimmers.  Remove resulting plant debris from site.

.10	Edging: use a steel bladed power edger to mechanically cut and provide neat, uniform, and well-defined appearances along all sidewalks, curbs, and other hard surfaces.  String line trimmers shall not be used for turf edging.  Provide edging services each month during June, July, August and September as necessary.  Remove edging debris after each edging operation.

.11	Ditches: trim grass using a mechanical trimmer at height no lower than 100 mm in ditches that are not accessible to mowers.  Where directed by Property Manager, allow selected ditches to remain natural in appearance.

.12	Contractor shall immediately repair or replace damaged turf and plants including damages to other site features resulting from improper and negligent use of string trimmers, mowers and other equipment.  Promptly advise Property Manager of all damages.

# 3.4	TREE AND SHRUB MAINTENANCE

.1	Monitoring:

.1	Regularly monitor and visually inspect the health and care of all plants on site to ensure proper and adequate plant care is provided in accordance with specifications.

.2	Indicate results of each plant monitoring inspection in maintenance log.

.2	Maintenance of Plant Beds and Tree Wells:

.1	Provide proper maintenance to all plants and plant beds each week as necessary.  Ensure healthy and vigorous growing conditions and aesthetically clean and pleasing site appearances are provided.

.2	Cultivate all non-mulched plant beds and tree wells in upper 40 mm of soil as necessary to maintain a loose friable soil free of foreign plant growth.  Do not damage roots of plants when cultivating.  Do not mound soil around base of tree trunk following tree well cultivation.

.3	Collect and remove all litter, debris, rubbish, animal waste and foreign plant growth weekly.  Remove all dead and unhealthy small plants as necessary.  Dispose of collected materials off-site.  Collect and remove all exposed rocks larger than 12 mm in diameter from planted areas and dispose off-site.

.4	Remove and eliminate perennial grass and weeds from all planted beds, tree wells and mulched areas weekly.  Control weeds by hand-weeding and use of contact spray herbicides.  Apply herbicides in accordance with manufacturer’s instructions and with Property Manager’s approval.  Verify that herbicide is appropriate for use with existing plant materials.  Contractor shall be responsible for any damages incurred as a result of improper herbicide use.

.5	Edge and maintain neat, clean and circular tree wells of loose friable soil each month where tree wells already exist and on coniferous plants.  Coniferous trees shall have a neatly cut and maintained edge at the dripline area with the well area kept clean and weed free.  Remove and eliminate grass adjacent to deciduous tree trunks (when necessary) to prevent damage from turf maintenance equipment.  Do not damage or cut roots of plants when edging or cultivating tree well areas.

.6	Edge along all plant beds and hedges evenly to depth of 100 mm to maintain original line and shape.  Use a sharp spade to make clean and neat angled cuts each month or as necessary.  Where plants have outgrown the original plant bed, enlarge the plant bed by edging and removing all turf to outside edge of plant growth.  Remove all resulting debris from site.

.7	Place fertile topsoil in plant beds to correct any low and uneven areas.  Place and level topsoil to fill former tree pits to grade in turf areas and spread grass seed.

.8	Tree Grates:  (where applicable) remove all tree grates each month and thoroughly clean the planted well area.  Collect, remove and eliminate all weeds, debris and other rubbish.  Replace grates after completion.  Cut and resize tree grates when necessary or directed by Property Manager to prevent girdling and other damage to tree trunks.  Maintain 50 mm spacing between plant tissue and tree grate metal.

.9	Rake, level and re-spread existing wood mulch to achieve a fresh appearance and to correct any disturbances, monthly.  Clean and remove all debris, litter, perennial weeds, grass and other foreign matter from all mulched areas weekly.

.10	Additional As-Required Work: supply and installation of new shredded pine bark mulch to minimum depth of 100 mm shall be considered as additional as-required work in contract when requested by Property Manager.  Contractor shall submit cost estimate for Property Manager’s review and approval.

.3	Staking and Tree Protection:

.1	Install or keep required stakes and guy wires taut and plants plumb during maintenance period, where required.  Repair guy wires when required.

.2	Remove existing support stakes and accessories on trees that are self-supporting or when directed by Property Manager.  Cut and remove any exposed wire basket, metal stakes and guying materials from tree base.

.4	Pruning:

Contractor Responsibilities In Contract: pruning of shrubs and other perennial plants shall be the responsibility of the Contractor in contract.

Additional As-Required Work: tree pruning requirements, however, shall be considered as additional as-required work in contract if requested by Property Manager.   Contractor shall submit cost estimate for specified tree pruning requirements based on either an hourly rate or a lump sum rate as directed by Property Manager.  Tree pruning services shall only proceed upon Property Manager’s approval.  Property Manager reserves the right to obtain competitive quotes from other arborist contractors that specialize in this service.

.1	Prune in accordance with proper practices and standards described in “Pruning in Alberta” and “ANSI A300” (International Society of Arboriculture) and as directed by Property Manager.  Property Manager will be the "Sole Judge" for assessing all pruning operations.

.2	Prune to provide natural branching structure and to encourage a healthy natural growth pattern.  Do not clip shrubs and other plants into balled or boxed forms as this type of pruning will be considered improper and unacceptable.

.3	Use sharp pruning tools and other equipment to prune plants without tearing and ripping plant tissue.  Sterilize pruning tools after completion of each plant cutting operation and especially after pruning diseased plants.

.4	Major pruning of trees shall be performed by Certified Arborists.  Trained, competent and knowledgeable gardeners, horticulturists and other staff shall perform shrub and other required pruning.  Submit credentials of each individual who will perform plant pruning services for Property Manager’s approval.

.5	Trees:  prune and remove dead, diseased, and damaged branches.  Prune and eliminate crossing, rubbing and obstructing branches.  Remove existing stubs, suckers, and water sprout growth.  Maintain adequate branch clearance.  Ensure coniferous trees have one dominant central leader where feasible.

.6	Shrubs:  prune shrubs to maintain a natural form and healthy looking appearance.  Rejuvenate older shrubs by removing mature stems and unproductive wood at ground level.  Thin and remove crowded, crossing and rubbing stems and branches.  Remove all dead, diseased, damaged and undesirable branches.  Clear all plant growth that has overgrown public sidewalks while maintaining a reasonably balanced appearance.  Pinch back new candle growth every spring on plants such as Mugo Pine.

.7	Hedge Plants:  (where applicable), trim and shear hedges in late June and August.  Use sharp hedge pruning tools to maintain a neat, clean and attractive appearance at height established by Province.  Cut and remove all dead and diseased stems at base.  Remove all foreign ornamental sapling growth including roots growing within the hedge plantings.  Hedge trimming shall be straight and even.  When necessary, hedge plantings shall be sheared to ground level to rejuvenate plant growth and control pest infestations.

.8	Shearing/Topping:  do not shear or top any shrub or tree except for hedging plants unless authorized by Property Manager.

.9	Remove all pruned wood, cuttings, diseased limbs and branches, debris and excess material off site to approved disposal location.

.10	Replace improperly pruned plants if directed by Property Manager.  Replacement plant shall match existing in size unless approved otherwise by Property Manager.

.5	Soil Conditioning:

Additional As-Required Work:  soil conditioning shall be considered as additional as-required work in contract when requested by Property Manager.  Contractor shall submit cost estimate to perform work in accordance with any applicable soils report or as directed by Property Manager. Work shall only proceed if approved by Property Manager.

.6	Plant Removals:

Additional As-Required Work: removal of dead, unhealthy and unsuitable trees and large shrubs shall be considered as additional as-required work in contract if requested by Property Manager.  Contractor shall submit cost estimate for all required plant removals that will include removal of stumps and roots (where practical) and all restoration requirements as directed by Property Manager.  Work shall only proceed if approved by Property Manager.  Property Manager reserves the right to obtain competitive quotes from other contractors that specialize in this service.

.7	Fertilization Requirements in Early Spring:

.1	Apply plant fertilizer as directed or in accordance with soil test analysis (if applicable).  Use controlled or slow release plant fertilizers only.  Notify Property Manager prior to commencement of fertilization applications.  Record all fertilization activities in maintenance log.

.2	Trees:  apply 10-6-4 or similar plant fertilizer to all non-mature trees by June 1st at rate of 18 g/25mm of tree caliper.  Use a deep root feeder, if necessary, in application of plant fertilizer and water to dripline area to ensure plants are thoroughly fertilized and watered.  Alternatively, place 16-10-9 or similar fertilizer spikes in ground at rate of one spike per 25 mm of caliper per tree around dripline of tree.

.3	Mature and established trees in turf areas exposed to adequate applications of turf fertilizer do not require supplementary fertilization unless directed otherwise.

.4	Plant Beds – Ornamental Plants:  spread 19-6-12 Osmocote or similar controlled release granular fertilizer by June 1st in accordance with manufacturer’s specified rate of application into upper surface of all planting beds.  Lightly rake into soil as applicable.  Record all fertilization in maintenance log.

.5	Ensure adequate water is applied after fertilizing to ensure penetration of fertilizer into soil and roots.

.8	Watering of Plants:

Contractor Responsibilities In Contract:  monitoring of plant conditions, operating site irrigation system to provide necessary moisture to plants and applying water by hand using any available building source (hose bibs) shall be the responsibility of the Contractor in contract.

Additional As-Required Work: - the application of water for plants using water trucks and a supply of water by Contractor shall be considered as additional as-required work in contract when requested by Property Manager.  Contractor shall submit cost estimate for the supply, application and trucking of water, including labour and other accessories for Property Manager’s review and approval.  Contractor’s cost estimate shall be based on either an hourly rate or per truck load as directed by Property Manager.  Service shall only proceed upon Property Manager’s authorization and approval of cost.  Property Manager reserves the right to obtain competitive quotes from other contractor’s if necessary.

.1	Monitoring:  regularly test and monitor soil moisture conditions and a plant’s need for water to ensure adequate health and survival.  Natural rainfall, site irrigation, plant maturity and specie shall be considered in determining amount and frequency of watering or if additional watering is necessary.  Regularly review plant watering needs with Property Manager to ensure the Property Manager has adequate information in determining if additional water is necessary.

.2	Watering shall be provided when necessary but especially during periods of warm weather and dry soil conditions to ensure healthy plant growth.  Contractor shall supply all necessary hose equipment of sufficient length including other accessories in use of building hose bibs.

.3	Watering Frequency Guidelines: to ensure plants grow in a healthy and reasonably non-stressed condition use the following watering guidelines in determining watering frequency for selected plants on site.  However, watering frequencies may be dependent on Property Manager’s approval of additional as-required work in contract:

.1	Established Trees: thoroughly deep root water individual selected trees located within zone 1 turf maintenance areas including existing trees located in tree grate locations minimum once monthly or as directed by Property Manager.

.2	Newly planted trees (five years and under – if applicable): thoroughly deep root water all new trees located throughout the site every two to three weeks when necessary.

.3	Established shrubs, ornamental grass and perennials:  thoroughly water all  plants minimum every two weeks when necessary or as directed by Property Manager.

.4	Newly planted shrubs, perennials and other plants (five years and under - if applicable) shall be watered minimum twice a week when necessary.

3.5		ANNUAL PLANT BED MAINTENANCE

Additional As-Required Work: - the supply, installation, and maintenance of annual flowering plants shall be considered as additional as-required work in contract when requested by Property Manager.  Contractor shall submit a lump sum cost estimate covering all required work for Property Manager’s review and approval.  Work shall only proceed if approved by Property Manager.  Property Manager reserves the right to obtain competitive quotes from others if necessary.

.1	Annual Plant Bed/Container Spring Preparations:

.1	Thoroughly clean annual plant beds and planters of all foreign matter, litter, rock chips, gravel, weeds, grass and other foreign plant growth.  Remove all contaminated plant bed soils.

.2	Cultivate (roto-till) planting soils to a minimum depth of 200 mm.  Hand cultivate small planters and containers.

.3	Place approved premium garden soil mix specifically blended for annual plants to correct any uneven or low area and to replace all plant bed soils removed from site.

.4	Apply 8-12-6 slow release granular fertilizer at rate of 4 kg/100 m2 and work into soil.  Rake soil level and lightly water.

.5	Obtain Property Manager‘s approval of plant bed/container preparations before installing any annual flowering plants.  Complete preparation of planting areas by May 20th.

.2	Installation and Maintenance:

.1	Install flowering plants in accordance with approved planting layout only after planting areas have been approved by Property Manager.

.2	Space annual flowers about 150 mm on centre to achieve a full, complete and appealing appearance.  Space individual larger growing plant species accordingly.  Complete installation by June 1st or when threat of frost has passed.

.3	Fertilizer:  apply 20-20-20 fertilizer to flowering plants every two weeks during the growing season.  Record all applications of fertilizer in maintenance log.

.4	Deadhead faded flowers each week to ensure continuous blooms.

.5	Lightly cultivate plant bed soil each week to maintain a loose friable soil free from perennial weeds and grass.  Do not damage flowering plants when cultivating or hand weeding.  Keep annual plant beds and planters free of all foreign plant growth.

.6	Regularly collect and remove all litter, debris and other foreign matter from plant beds and planters.  Keep plant beds and planters free of all foreign debris and litter.

.7	Perennials:  divide crowded and overgrown perennial plants on site, (where applicable), and replant during spring season as directed by Property Manager.  Thoroughly water all plants after replanting and every week thereafter until well established.

.8	Watering:  frequently and thoroughly hand water all flowering plants as necessary to maintain adequate moisture within root systems and for healthy vigorous growth.  Provide clean water, water truck and all accessories as necessary to adequately water plants.  Contractor will be expected to water flowering plants seven days a week when necessary.  Never allow planting soils to dry out.  Record all applications of water in maintenance log.

.9	Pest Control:  apply appropriate pesticides when necessary to control specific disease and insect infestations on annual and perennial plants.  Pick and remove weeds from plant beds and planters on an ongoing weekly basis.

# 3.6	INTEGRATED PEST MANAGEMENT

.1	Integrated Pest Management (IPM):

.1	Property Manager supports the management and control of pests using IPM principles that utilizes regular monitoring to identify pests, considers various control options (biological, physical, cultural, mechanical and chemical) before implementing an effective, economical and environmentally acceptable solution to prevent and suppress pests.

.2	Use IPM principles to reduce or eliminate a reliance on chemical pesticides.

# 3.7	PESTS: WEED, INSECT AND DISEASE CONTROL

Contractor Responsibilities In Contract: - Contractor shall be responsible for monitoring site in contract for pests and advising the Property Manager of all potential pest problems.

Additional As-Required Work: - supply and application of chemical pesticides to control pests shall be considered as additional as-required work in contract.  Contractor shall submit cost estimates based on either an hourly rate or a lump sum rate as directed by Property Manager to supply and apply pesticides when deemed necessary.  Service shall only proceed upon Property Manager’s authorization and approval of cost.  Property Manager reserves the right to obtain competitive quotes from other contractor’s that specialize in this service.

.1	Pest Monitoring:

.1	Pest Monitoring:  regularly monitor and visually inspect all plants, turf and other landscape areas to identify potential pest problems and determine appropriate pest controls.  Pest problems include insect, disease and weed infestations that pose a serious and on-going threat to plant life on site.

.2	Ensure proper, positive identification of infestations.

.3	Indicate results of monitoring inspections in maintenance log.  Review all pest concerns with Property Manager.  Record all actions taken in control of pest problems in maintenance log.

.2	General Conditions:

.1	Use of chemical pesticides are restricted as Property Manager supports the use of Integrated Pest Management (IPM) practices.  Advise Property Manager on whether IPM practices and techniques are practical or effective in managing and controlling any existing pests on site or if chemical pesticides are necessary.

.2	Determine the susceptibility of plant species to pesticide damage before requesting use of chemical pesticides.  Request Property Manager’s approval of chemical pesticide use where deemed necessary in the management and control of pest infestations.

.3	Applications of pesticides shall be performed in accordance with Alberta Environment’s current legislation.  Provide Property Manager with three days advance notification of intent to apply chemical pesticides on site.

.4	Use equipment and containers free of harmful residues not related to specific control measures applicable to situation.

.5	Certified Applicator:  when pesticides are deemed necessary to control pests, the application of each pesticide on site shall be performed by a certified pesticide applicator.  Personnel assisting the certified applicator on site shall be thoroughly trained and knowledgeable in pesticide applications and use of all equipment in accordance with Alberta Environment’s Code of Practice for Pesticides.  Applicator shall maintain pesticide application record books and submit at completion of each pesticide application.

.6	Prepare and apply pesticide according to manufacturer's specifications.  Minimize drift at all times.  Erect signs to notify building occupants and the public regarding pesticide use on site.

.7	Timing:  pesticides shall be applied at times, which limit any possibility of contamination from climatic and other factors.  Monitor weather conditions to avoid making application prior to inclement weather to eliminate potential runoff from treated areas.  Confine all applications to outside of regular site operation hours to avoid contamination from drift and its effect on surroundings, occupants of nearby buildings and site users.

.3	Pest Controls:

.1	Weeds:

.1	Weed control and eradication methods shall be continuous and ongoing during active growth and establishment.  Ensure weed seed heads are removed before maturity.  Implement IPM practices and techniques that include cultivation and physical methods where practical before requesting use and applying chemical pesticides.

.2	Eliminate and remove from site all noxious weeds in accordance with government regulations.

.3	Ensure thorough and effective controls are implemented to eliminate all weed growth on site.

.2	Insects and Disease:  apply pesticides based on development stage of insects' life cycles to prevent loss or damage to plant material.  Monitor turf areas and plants and apply approved pesticides to control pest infestations if IPM practices and techniques are not effective.

.3	Monitor effectiveness of each pesticide application and promptly correct any inadequate or deficient application.

.4	Repair and pay for damage caused by application of herbicides.

.5	Do not use soil sterilants.

# 3.8	IRRIGATION SYSTEM

Note: - maintenance of site irrigation systems, where applicable, shall be the responsibility of a specialized irrigation contractor under contract to the Property Manager.  Grounds contractor shall co-operate and coordinate work of the grounds maintenance contract with the Property Manager to ensure site irrigation system is set, adjusted and maintained to suit the needs of the grounds maintenance contract and site landscape.  Grounds contractor shall be expected to perform regular visual inspections of the site irrigation system while in performance of contracted grounds maintenance services and promptly inform the Property Manager of any deficient or defective irrigation equipment or operation on site.  Property Manager’s irrigation contractor shall be responsible for correcting and repairing all deficient irrigation equipment and operations.

# 3.9	AUTUMN PREPARATION

.1	Leaf Removal:  rake and vacuum fallen leaves, as necessary each week, and remove to an approved waste recycling depot.  Continue until leaves cease to fall.

.2	Clean all plant beds, planters, tree wells, mulched areas, and other landscaped areas weekly, as necessary.  Remove collected debris from site.

.3	Sweep and clean all walkways and other hard surface areas weekly.  Keep catch basins, drains, and all curbs and gutters free of plant debris and other litter.  Remove all collected debris and litter from site.

.4	Remove all annuals (as applicable) and cut back foliage of perennial plants following freezing weather conditions.  Deep cultivate all plant/annual beds and planters.  Replenish plant beds with fertile topsoil where settlement occurs.

.5	Additional As-Required Work:  power sweeping of all paved roadways, parking areas and other hard surfaces in autumn shall be considered as additional as-required work if requested by Property Manager.  Services shall generally be completed by October 1st or as directed by Property Manager.  Contractor shall submit cost estimate for Property Manager’s approval and authorization of power sweeping services.

.6	Additional As-Required Work: deep root watering of trees, shrubs and other plants by mid-October shall be considered as additional as-required work in contract when requested by Property Manager.  Contractor shall submit cost estimate regarding the supply and application of water, including trucking, labour and other accessories for Property Manager’s review and approval.  Record total quantity of water applied on site including locations of watering activity in maintenance log each day that service is provided.

# 3.10	CLEANLINESS OF GROUNDS

.1	Site grounds shall be kept in a clean and tidy condition.  Provide weekly clean-up services to ensure aesthetically pleasing and desirable site appearances are continually maintained.  Sweep, clean, collect and remove all debris, litter, rubbish and pests each week in maintenance of site grounds.

.2	Provide prompt service within three (3) hours when directed by Property Manager to correct or complete clean-up services deemed inadequate or incomplete.

.3	Dispose of all collected litter, material and other debris off site to municipal disposal site following each clean-up activity.  Contractor shall pay all off-site disposal costs.  Do not dispose of any debris in Property Manager’s on-site disposal bins.

.4	Sweep and clean all building entrances/exits, stairs, sidewalks, handicap/wheelchair access, along all curbs and gutters, and from all other hard surface areas to remove all litter and foreign debris.

.5	Hand scrap and/or pressure wash hard surfaces to remove gum, soil and other foreign matter when necessary to maintain clean appearances.

.6	Empty all trash receptacles weekly or as required based on usage.  Supply and replace heavy duty refuse bags after each trash removal and clean-up.

.7	Keep all site furnishings, signage and monuments in a clean and sanitary condition.   Clean cigarette snuffers and other ashtray furnishings.

.8	Remove all accumulated debris and other litter from all catch basins and other drains on site weekly.

.9	Keep washed rock, gravel, and wood mulched surfaces clean and free of all debris, litter, weeds, grass and other foreign plant growth weekly.

.10	Make regular inspections for vandalism and damage.  Immediately report vandalism and damage to Property Manager and note in Maintenance Log.

# END OF SECTION

### Schedule ‘A’ - GROUNDS MAINTENANCE LOG

SITE:	_________________________________________________________

(CONTRACTOR MUST COMPLETE WITH EACH SITE VISIT)

#### DATE: ______________	   CONTRACTOR: ______________________________________

SITE SUPERVISOR: ______________________________  NUMBER OF WORKERS ON SITE: _________

LOG RECORDED BY: ____________________________________________________

START TIME: ____________ (am/pm)    COMPLETION TIME: ___________ (am/pm)

WEATHER CONDITIONS: ______________________________________ and _______________◦C

## Turf Maintenance:

Mowing: Zone 1  ☐  ‪/ Zone 2  ‪☐  / Zone 3  ☐  /  Turf Trimming  ☐  Grass/Site Clean-Up  ☐ ‬‬‬‬‬‬‬‬‬‬‬‬ Watering  ☐

Turf Edging:  Walkways  ☐  /  Concrete Curbs  ☐       Turf:  Aeration  ☐  /  Dethatching   ☐    Turf Repairs  ☐

Pest Control   _________________________________________________________________ (Specify)‬

( Indicate Pests Controlled / Pesticide Applied  )

‪‬‬‬‬‬‬

Fertilizer  ‪ ____________________________________________________________________ (Specify)‬‬‬‬‬‬

( Indicate Turf Areas Fertilized / Fertilizer Type / Quantity (kg) Applied / Rate of Application )

Plant Maintenance:

Plant Bed:  Cultivation  ☐  / Weeding  ☐  / Clean-Up  ☐‪        Tree Well: Cultivation  ☐  / Weeding  ☐  ‬‬‬‬‬‬

Pruning:  Trees  ☐  /  Shrubs  ☐      Plant Removals   ☐            Edging:  Plant Beds  ☐   /  Tree Wells  ☐

Plant Watering  ☐             Clean-Up  ☐         Annual Plant Bed Preparation  ☐     Deep Root Watering   ☐

Quantity of Water Supplied/Applied Per Visit   _________________________

Annual Flowers:  Supply/Installation  ☐  /  Watering  ☐  /  Fertilizer  ☐  /  Cultivation & Weeding  ☐

Pest Control:  __________________________________________________________________ (Specify)‬

( Indicate Pests Controlled / Pesticide Applied  )

Fertilizer:  _____________________________________________________________________ (Specify)‬

( Indicate Plants Fertilized / Fertilizer Type / Amount (kg) Applied / Rate of Application )

Site Clean-Up/Preparation:

Clean & Sweep:  Sidewalks  ☐  /  Building Entrances  ‪☐  /  Stairs  ☐  /  Delivery/Loading  ☐  /  Roadways  ☐  ‬‬‬‬‬‬

/  Parking Lots  ☐  /  Curbs & Gutters  ☐               Clean & Weed Rock / Wood Mulched Surfaces  ☐  ‬‬‬

Site Litter & Debris Removal  ☐      Pressure Wash Hard Surfaces  ☐     Clean Trash Receptacles‪  ☐ ‬‬‬  ‬‬‬

Spring Clean-Up & Preparation  ‪☐   /   Mechanical Power Sweep  ☐  ‬‬‬‬‬‬

Autumn Clean-Up & Preparation  ☐  /   Leaf Removal  ☐   /   Autumn Deep-Root Watering  ☐

Other:  ‪_______________________________________________________________________ (Specify)

Note:  All Work of Contract Has Been Completed To Date As Specified?    Yes  ☐      No  ☐

##### Repairs/Other Work/Comments:    ________________________________________________________

_____________________________________________________________________________________

_____________________________________________________________________________________

____________________________________________    Signature: _____________________________