Section Cover Page

Section 08990 2005-02-08 Major Window Cleaning Services

Use this Section to specify requirements for window cleaning that requires the use of suspended platforms, scaffold towers, or other specialized cleaning equipment to be operated by window cleaners who are trained in the rigging and operation of such equipment.

When window surfaces can be cleaned without the use of specialized equipment or personnel, use Section:  Minor Window Cleaning Services.

This Master Specification Section contains:

- This Cover Sheet

2.	Specification Section Text:

1.	General

1.1	Intent

1.2	Related Requirements

1.3	Reference Standards

1.4	Operation and Maintenance Data

1.5	Window Cleaner Qualifications

1.6	Regulatory Requirements

2.	Products

2.1	Materials

3.	Execution

3.1	Manufacturer's Instructions

3.2	Verification of Conditions

3.3	Protection of Public

3.4	Protection of Existing Finishes

3.5	Erection of Window Cleaning Equipment

3.6	Operation of Window Cleaning Equipment

3.7	Window Cleaning:  Generally

3.8	Clean-Up

Editing:  Use this Section as is; do not modify in any way.

1.	General

1.1	INTENT

.1	This Section includes requirements for window cleaning that requires the use of suspended platforms, scaffold towers, or other specialized cleaning equipment to be operated by window cleaners who are trained in the rigging and operation of such equipment.

1.2	RELATED REQUIREMENTS

.1	Refer to Major Window Cleaning Materials, Equipment and Location Schedule for:

.1	materials and equipment to be provided by Minister, and

.2	property locations where services are to be performed.

1.3	REFERENCE STANDARDS

.1	Comply with the requirements of the following standards when applicable to the window cleaning operations:

.1	CSA Z91-M1980 - Safety Code for Window Cleaning Operations

.2	CAN3-Z271-M84 - Safety Code for Suspended Powered Platforms

1.4	OPERATION AND MAINTENANCE DATA

.1	Obtain applicable operation and maintenance data in the Minister's possession for window materials and equipment involved in the tasks of this Section.

1.5	WINDOW CLEANER QUALIFICATIONS

.1	Only window cleaners who are trained and have demonstrated their competence in the rigging and operation of appropriate window cleaning and safety devices shall perform window cleaning tasks on suspended platforms, powered platforms, single point suspension chairs, harnesses and cages, wheel mounted aerial devices or site-erected mobile-wheeled scaffold towers.

1.6	REGULATORY REQUIREMENTS

.1	Comply with Alberta Workers' Health, Safety & Compensation Regulation pertaining to the use of scaffolding, work platforms and temporary supporting structures.

2.	Products

2.1	MATERIALS

.1	Provide cleaning materials and supplies not provided by Minister:  non-abrasive to glazing surfaces and non-hazardous to window cleaners.

3.	Execution

3.1	MANUFACTURER'S INSTRUCTIONS

.1	Comply with manufacturer's instructions for:

.1	the operation of window cleaning equipment,

.2	methods and cleaning materials to be used for cleaning of special glazing materials including applied interior glazing film.

3.2	VERIFICATION OF CONDITIONS

.1	Ensure proper operation of window cleaning equipment in accordance with CSA Z91-M1980 and CAN3-Z271-M84.

.2	Where building is equipped with window cleaning equipment, obtain copy of 3 month inspection and test report.  Ensure deficient items have been corrected.

.3	Report all window cleaning equipment defects to Minister.

.4	Report caulking defects, broken and cracked glazing units to Minister.

3.3	PROTECTION OF PUBLIC

.1	Protect public and building users from hazards with respect to window cleaning chemicals and window cleaning equipment.

.2	Ensure safe passage of persons around and below areas of window cleaning operations.

.3	Install temporary barricades, guardrails and signs to protect public.

.4	Consider prevailing weather conditions and weather forecasts.  Cleaning of exterior side of exterior windows shall not proceed when weather conditions constitute a hazard to workers, equipment, or property.

3.4	PROTECTION OF EXISTING FINISHES

.1	Provide temporary protection to adjacent building finishes from adverse effects of window washing chemicals and equipment.

3.5	ERECTION OF WINDOW CLEANING EQUIPMENT

.1	Where building is not equipped with window cleaning equipment, erect appropriate equipment in accordance with CSA Z91-M1980 and CAN3-Z271-M84.

3.6	OPERATION OF WINDOW CLEANING EQUIPMENT

.1	Operate window cleaning equipment in accordance with manufacturer's instructions and CSA Z91-M1980.

.2	Do not overload window cleaning equipment.

3.7	WINDOW CLEANING:  GENERALLY

.1	Washing and polishing of glass and window surfaces, including head, sash, sills, sun and insect screens shall remove all grit, dust, dirt, stains, insects, fingermarks, streaks, spots, cloudy film and graffitti.

3.8	CLEAN-UP

.1	Remove temporary window cleaning equipment.

.2	Return building window cleaning machinery and equipment to proper storage mode and location.

.3	Remove all cleaning chemicals and supplies.

END OF SECTION