Section Cover Page

Section 12821 2005-02-08 Interior Plant Maintenance

Use this Section to specify requirements for interior plant maintenance.

This Master Specification Section contains:

.1	This Cover Sheet

.2	Specification Section Text:

1.	General

1.1	Related Requirements

1.2	Regulatory Requirements

1.3	Reference Standards

1.4	Delivery, Storage and Handling

1.5	Damage to Property

1.6	Hours of Work

1.7	Maintenance Log

2.	Product

2.1	Fertilizer

3.	Execution

3.1	Interior Maintenance - Generally

3.2	Plant Maintenance

3.3	Weed, Insect and Disease Control

3.4	Cleanliness of Planting Areas

3.5	Plant Replacements

Editing:  Use this Section as is; do not modify in any way.

1.	General

1.1	RELATED REQUIREMENTS

.1	Refer to Interior Plant Maintenance Material, Equipment and Location Schedule for:

.1	where operations specified in this Section are to be performed,

.2	any materials or equipment to be supplied by the Minister, and

.3	normal hours of work during which the specified services shall be performed.

1.2	REGULATORY REQUIREMENTS

.1	Provide Minister with copies of permits and licences required by regulatory authorities, including pesticide applicator's current pesticide licence number, Class 'J'.

1.3	REFERENCE STANDARDS

.1	Pruning methods:  Pruning in Alberta Manual, Alberta Adgex 270/24-1

.2	Interior Plant Care Workbook by Alberta Infrastructure and Transportation.

1.4	DELIVERY, STORAGE AND HANDLING

.1	Deliver and store fertilizer and seed in waterproof bags showing mass, analysis and name of manufacturer.

.2	If required, provide storage space additional to the available space at the site for material and equipment.

.3	The contractor shall be responsible for the storage of pesticides.

1.5	DAMAGE TO PROPERTY

.1	Contractor shall repair and pay for damages caused by contractor's personnel and equipment during the term of the Contract.

.2	Contractor is to report damages immediately to Minister.

.3	Obtain Minister's approval for repairs and replacements.  Return plant materials, equipment and buildings to their original condition prior to damage.

.4	Complete repairs and replacements within seven days from date of approval given for repair or replacement.

1.6	HOURS OF WORK

.1	Perform pesticide application outside of regular working hours, with Minister's approval.

.2	Notify Minister three days in advance of intent to undertake pest, insect and disease control operations.  Do not undertake operations unless approval to do so has been given by Minister.

.3	Obtain Minister's approval for tasks to be performed after regular hours.  These tasks may include major pruning, leaching and soil requirements.

1.7	MAINTENANCE LOG

.1	Keep Maintenance Log at client's office on-site throughout contract.

.2	Submit daily log to Minister at each site inspection meeting.

.3	Include in Log:  detail activities, areas in which activities were carried out, and approximate time for completion of each activity.

.4	Detail applications of pesticides in Maintenance Log.  Include insect, mode, type and rate of application of pesticide, date, time, weather conditions and results of application.

.5	In planting beds, planters and tree wells, test soil mix for pH, total salts, and major and minor nutrients of soil twice per year.  File soil analysis and corrective measures taken in Log.

.6	Test soil moisture monthly or at Minister's discretion and record in Log.  Tests will be taken by Minister before and after watering.

2.	Products

2.1	FERTILIZER

.1	Fertilizer:  according to results from semiannual soil test and seasonal requirements.

.2	Fertilizer:  analysis of  20-20-20 for seasonal flowers.

3.	Execution

3.1	INTERIOR MAINTENANCE - GENERALLY

.1	Schedule timing of operations to use of building and to locations of plants in offices and building.

.2	Do each operation continuously and complete within three days.

.3	Provide material and equipment necessary for continuous maintenance to current acceptable horticultural standards.

.4	Provide safety precautions while working in all areas.

.5	Cooperate with Minister.  Maintenance practices may have to be altered to deal with program requirements.

.6	Collect and dispose of excess material and debris off-site weekly.

.7	Obtain approval, from Minister, in writing, for work done and accepted before submitting progress claim.

3.2	PLANT MAINTENANCE

.1	Watering:

.1	Monitor moisture levels of individual plant species and provide adequate water supply by hand.

.2	Supply water at 18(C for surface and deep root methods on large specimen trees.

.3	Supply water at 18°C to individual potted specimens once per week or as required to maintain optimum level of moisture.

.2	Cultivation of Plant Beds and Planters:

.1	Cultivate upper 40 mm of soil weekly.

.2	Remove weeds by hand only including their roots.

.3	Do not damage roots of plants.

.3	Fertilization Requirements:

.1	Use water soluble fertilizer to assure optimum plant growth.

.2	Use fertilizer recommended in soil analysis.

.4	Pruning:

.1	Obtain Pruning in Alberta Manual from Alberta Infrastructure and Transportation at time of start-up meeting.

.2	Prune and thin plantings in accordance with Manual.

.3	Observe and remove dead or unhealthy foliage and flowers at least once per week.

.5	Leaching:

.1	Leach potted plants every six months to prevent buildup of salts in soil.

.2	For plants which cannot be leached, water plants with a 1% sugar solution once every two weeks as part of the regular watering program.  Provide a cycle of 4 applications every 6 months.

.6	Cleaning of Foliage:

.1	Clean foliage thoroughly every six months with 18°C water.  Methods can be syringing, power spraying or hand washing.

.2	Do not use plant shine.

.7	Staking:

.1	Keep stakes and guy wires taut and plants plumb for duration of maintenance period.

.8	Seasonal Plants:

.1	Remove seasonal plants when seasonal requirements are satisfactorily completed.

3.3	WEED, INSECT AND DISEASE CONTROL

.1	General Considerations:

.1	Ensure proper, positive identification of infestations and consult with Minister before taking corrective measure.

.2	Prior to spraying, obtain written approval from Minister.

.3	Determine susceptibility of plant species to pesticide damage prior to any chemical application.

.4	Use equipment and containers free of harmful residues not related to specific control measures applicable to situation.

.5	Perform disease and insect control, when necessary, in accordance with Provincial pesticide application regulations.  Notify Minister of intent at least three days prior to any pesticide application.

.6	Prepare and apply pesticide according to manufacturer's specifications.  Minimize drift at all times.

.7	Carry out treatment with due regard to climatic conditions' effect on surroundings and occupants of buildings.

.2	Insect and Disease Control:

.1	Make weekly inspection of plants and control insect and disease infestations.  Development stage of insects' life cycles shall determine dates of pesticide applications.

.2	Repair damage caused by application of pesticides.

.3	Carry out appropriate control program by hand.

.4	Effectiveness of treatment program to be determined by inspection by Minister.  Repeat as required.

3.4	CLEANLINESS OF PLANTING AREAS

.1	Keep areas in clean and tidy condition, daily.

.2	Clean hard surface and carpets after each maintenance operation.

.3	Obtain Minister's approval for cleaning treatments required.

.4	Report any vandalism or damage to Minister immediately.

3.5	PLANT REPLACEMENTS

.1	Replace dead and unhealthy plants which have occurred because of contractor's neglect or lack of maintenance.

END OF SECTION